## Slide 1: OMA Lightweight M2M V1.0 LWM2M
Jaime Jiménez, Ericsson Research
April 25th, 2015

## Slide 2: Table of Contents
Introduction
Bootstrapping
Registration Interfaces
  Register, Update, De-register
Device Management & Service Enablement
  Read, Discover (RFC6690), Write, Execute, Create, Delete
Information Reporting
  Observe, Notify, Cancel Observation
Identifiers and Resources
Data Formats
Security
  UDP/SMS channel bindings, GBA?
  Pre-shared keys, PKI, X.509
Access Control

## Slide 3: Introduction
There are 4 interfaces:
1. Bootstrap
2. Client Registration

## Slide 4: Introduction
There are 4 interfaces:
3. Device Management
4. Information Reporting

## Slide 5: Bootstrapping
There are 4 bootstrap modes:
  Factory Bootstrap (everything preconfigured)
  Bootstrap from Smartcard (information read from a smartcard, requires a secure channel btw smartcard and device)
  Client initiated Bootstrap (used when server is not configured in the client or initial config fails, the LWM2M Bootstrap Server will give the information. The server will use the write/delete to modify the information)
  Server Initiated Bootstrap (Just like before, but without the client sending request. The server already knows that the client is ready. How the server knows that is implementation specific.)

## Slide 6: Bootstrapping
The bootstrap sequence is the following:
  If device has Smartcard, the device tries to use it.
  If not, it tries the factory bootstrap.
  If none of the above and the server has LWM2M Server Object instances from the previous instances, then the device tries to register using them.
  If all those steps fails, and the client does not receive the server initiated bootstrap within the ClientHoldOffTime then it uses the client initiated bootstrap. The client must have the LWM2M Server Bootstrap Information (with at least one LWM2M Server account) after this step.

## Slide 7: Bootstrapping: Example
Client Initiated Bootstrap
  Client requests bootstrap, sending its endpoint name
  Server accepts and deletes existing content on device(“/” URI)
  Server creates Object Instance for LWM2M Server (/1/0)
  Server creates an Access Control Instance (/2/0)

## Slide 8: Registration
Register
  Client provides properties that the server needs to contact the client and maintain the session (e.g. EP name, lifetime, queue mode…) as well as objects in client.
Update
  Periodically done, updates lifetime of registration.
De-register
  When shutting down device or discontinuing the service.

## Slide 9: Registration - REGISTER
After bootstrapping, LWM2M initiates “Register” operation with the LWM2M Server. Parameters are:
  Endpoint Client name in URN format (e.g. “urn:imei:0800200c9a66”)
  Lifetime (default 86400 seconds)
  LWM2M Version (If > 1.0)
  Binding Mode. Either UDP(U) or SMS (S) And either Serial (S) or Queue (Q) modes. Queue mode means that the server queues all request to client while client is asleep.
  SMS Number (MSISDN) if SMS binding
  Objects and instances

## Slide 10: REGISTRATION: Example
Registration uses CoAP message types.
  Client Registers and specifies endpoint, lifetime, version and binding types.
  Server confirms the creation in Resource Directory.
  Client Updates modifies the lifetime.
  Client Deletes entry in Resource directory.

## Slide 11: Device Management & Service Enablement
Read
  Client provides properties that the server needs to contact the client and maintain the session (e.g. EP name, lifetime, queue mode…) as well as objects in client.
Discover (RFC6690)
  Using CoAP, GET to "/.well-known/core” returns a payload in the CoRE Link Format
Write
  Used to change value of Objects & Resources.

## Slide 12: Device Management & Service Enablement
Write Attributes
  These are use with the Observe/Notify operations, when changes on readable resources occur.
Execute
  Initiate action on individual resources.
Create
  Used to create and update objects. LWM2M Server will be the owner and has full access rights to the resource.
Delete
  Used when the LWM2M Server deletes an Object Instance within the LWM2M Client.

## Slide 13: INFORMATION REPORTING INTERFACE
Observe (Subscribe)
  Server initiates observation of Object Instance, monitoring changes in the write attributes (minimum/maximum period, >, <, step, cancel).
Notify (Publish)
  Client replies with Notification during observation process. Observation periods are defined in the Observe message.
Cancel Observation (Unsubscribe)
  Observation should be cancelled either by specifically sending a cancel observation message or by adding the cancel parameter in the attributes.

## Slide 14: IDENTIFIERS AND RESOURCES
Resource Model
  Everything is a resource. Resources are organized into objects. Objects define a grouping of resources for a purpose (e.g. Firmware upgrade, Error Report, …). Objects must be instantiated before they can be edited. Object Instances should have an Access Control
  Example below: Object Instance 0 has 2 Resources. Resource 1 supports r,w and x operations, Resource 2 only read. The client also has an associated Access Control Object Instance contains an Access Control List (ACL) that supports read an write on that particular object instance. However, writing in Resource 2 is not possible and in Resource 1 he will not be able to execute.

## Slide 15: IDENTIFIERS AND RESOURCES: Data formats
Identifiers
  Defined in 6.2 of LWM2M spec, table 16. Provides identifiers for all entities in the protocol: Endpoints, Bootstrap Server, LWM2M Server, Objects, Resources…
  In particular, Endpoints use URNs (urn:uid, urn:imei, urn:esn, … )
Data formats for transferring Resource Information
  Plain Text (if UTF8 r&w), Opaque (if binary r&w), TLV (if multiple instances), JSON.

## Slide 16: Security
Based on CoAP.
  Transport security based on UDP and SMS channel bindings.
  Authentication of communicating LWM2M entities is required:
    LWM2M Client MUST authenticate a LWM2M Server prior to exchange of any information.
    LWM2M Server MUST authenticate a LWM2M Client prior to exchange of any information.
    LWM2M Client MUST authenticate a LWM2M Bootstrap Server prior to exchange of any information.
    LWM2M Bootstrap Server MUST authenticate a LWM2M Client prior to exchange of any information.